## Slide 1: IDENTIFY Student Study Guide
R GUNNE R
COMM ON
MCAOSRTEE

## Slide 2: MASTER GUNNER COMMON CORE
VEHICLE IDENTIFICATION STUDY GUIDE
1.
Key identifiable features for all vehicles tested during MGCC.
2.
1.
2.
3.
Testable Material will include: Vehicle Name (Top of Slide)
Primary and Secondary Armament (Highlighted in Red Box) Ranges for Primary and Secondary Armament (Highlighted in Red
Box)

## Slide 3: T-72
Loading…
Grenade launchers on the R/S
Gunner’s night optics
22 round carousel auto-loader underneath crew compartment of turret
Gunner’s day optics
Brick shaped ERA
Single Driver periscope
7.62mm Coax
125mm MER: 3000m AT-11 Sniper MER: 4000m
Engine exhaust on the L/S

## Slide 4: T-72
Skirts has 4 rows of Brick shaped ERA
6 evenly spaced road wheels
Rear sprocket drive and supported track
IR search light No grenade launchers
on right side
Bore evacuator 1/3 away from the end of muzzle
Vehicle commander on the R/S with
12.7mm MG
Brick shaped ERA
Single driver periscope
Extended range fuel tanks

## Slide 5: T-80
Loading…
Add on armor & anti- armor RPG plates to protect turret ring
4 smoke grenade launchers on both sides
3 driver periscopes
Add-on armor plates front hull
Gunner’s day optics
Vehicle commander on the R/S wit
12.7mm MG
Gunner’s night optics behind day optics
28 round carousel auto-loader underneath crew compartment of turret
7.62mm Coax
125mm MER: 3000m
AT-8 Songster MER: 4000m

## Slide 6: T-80
1 & 2 paired road wheels
3 & 4 paired road wheels
Supported track rear sprocket drive
Turbine engine exhaust center rear
125mm gun can fire a radio guided missiles. Bore evacuator 1/3 from the end of the muzzle.
Add-on armor plates on front skirts
Anti-armor RPG plates to protect turret ring
Extended range fuel tank racks
Gunner’s day optics
Gunner’s night optics

## Slide 7: T-90
Gunner’s night optics
Gunner’s day optics
Vehicle commander on the R/S with
12.7mm MG
V-shaped cut add on armor around driver periscope
SHTORA optical jammer counter-measure vs. ATGMs
22 round carousel auto-loader underneath crew compartment of turret
Bulldozer blade
Laser warning receivers
7.62mm Coax
125mm MER: 3000m
AT-11b Sniper MER: 5000m

## Slide 8: T-90
6 evenly spaced road wheels
Rear sprocket drive and supported track
Engine exhaust on the L/S
3 segmented add-on armor plates on front skirts
KONTAKT 5 ERA on
front turret shape of a wedge
125mm gun can fire a laser
guided missile that can shoot down helicopters
SHTORA optical jammer counter-measure vs. ATGMs
V-shaped cut add on armor around driver periscope
Meteorological data collector

## Slide 9: BMP-2
Tube launch anti-tank guided missile
Speed boat shaped
hull with trim vane
Front sprocket drive supported track
Gap between #4, 5, & 6 road wheel
Troop periscopes for the gun ports
Top of the track is high in relationship to the hull
Bullet deflectors
Two man larger turret shape of a fry pan
Muzzle break on the end
30mm MER: 1500m
AT-5 Spandrel MER: 4000m

## Slide 10: BMP-2
Bullet deflectors
Skinny or thin tracks
Engine exhaust
Trim vane
Two man larger wide turret shape of a fry pan
IR search light
30mm MER: 1500m
AT-5 Spandrel MER: 4000m

## Slide 11: BMP-3
Loading…
Engine exhaust
Bow gunner hatch & 7.62mm MG
Bow gunner hatch & 7.62mm MG
Trim vane folds down
6 road wheels that have western style appearance
Driver center of hull
Vehicle commander Gunner
Two man flat wide turret shape of a fry pan
Square rear end
30mm MER: 2000m
100mm HE & AT-10 Stabber MER: 4000m

## Slide 12: BMP-3
6 road wheels that have western style appearance
Rear sprocket drive supported track
Hydro propulsion system
Can carry 6 troops
Gunner’s optics
Square rear end

## Slide 13: BMD-2
5 road wheels that are evenly spaced
Rear sprocket drive supported track
4 track support rollers
Bullet deflectors in front of driver
30mm long skinny gun and tube launch ATGM
One man small turret for VC/Gunner
Bow gunner MG port
30mm MER: 1200m
AT-5 Spandrel MER: 4000m
Sloped rear end

## Slide 14: BMD-2
30mm long skinny gun and tube launch ATGM
Sloped rear end
Engine exhausts
Hydro propulsion system
Distinct truck bed appearance in the rear
One man small turret for VC/Gunner
5 road wheels that are evenly spaced
Rear sprocket drive supported track
4 track support rollers
Muzzle break on the end

## Slide 15: BMD-3
30mm long skinny gun
Squared rear end
Engine exhausts
Distinct truck bed appearance in the rear
Two man turret with a lower profile
5 road wheels that look like trash can lids
Rear sprocket drive supported track
4 track support rollers
Distinct duck bill front slope
30mm MER: 1200m
AT-5 Spandrel MER: 4000m

## Slide 16: BMD-3
Squared rear end
5 road wheels that look like trash can lids
Rear sprocket drive supported track
4 track support rollers
Distinct duck bill front slope and it’s straight edge
Trim vane folds on top
30mm long skinny gun
Two man turret with a lower profile
Tube launch ATGM
Driver center of hull

## Slide 17: BTR-70
Distinct sloped rear- end and exhaust
One man turret with no over head hatch
Troop step up in between #1 & 2 wheels
Distinct duck bill front slope and it’s straight edge. Trim vane folds on top
Troop exit door
14.5mm MER: 2000m
Troop step up in between #3 & 4 wheels

## Slide 18: BTR-70
Distinct sloped rear- end and exhaust
One man turret with no over head hatch
Troop step up in between #1 & 2 wheels
Distinct duck bill front slope and it’s straight edge. Trim vane folds on top
Troop exit door
14.5mm MG
Troop step up in between #3 & 4 wheels
Twin eyelet windshields

## Slide 19: BTR-80 One man turret with no over head hatch
Exhaust rear-end is horizontally straight
Troop step up in between #1 & 2 wheels
Improved troop exit doors
Troop step up in between #3 & 4 wheels
14.5mm MER: 2000m
Distinct duck bill front slope and it’s straight edge. Trim vane folds on top

## Slide 20: BTR-80
One man turret with no over head hatch
Troop step up in between #1 & 2 wheels
Distinct duck bill front slope and it’s straight edge. Trim vane folds on top
Improved troop exit doors
14.5mm MG
Troop step up in between #3 & 4 wheels
Twin eyelet windshields
Exhaust rear-end is horizontally straight

## Slide 21: TYPE 96
Rear sprocket drive supported track
6 road wheels with gap between #1, 2 & 3
ERA side turret
Type 96 only has 2 engine exhausts on the R/S
Both sides of the turret has 6 smoke grenade launchers
ERA front glacis
125mm gun with a bore evacuator 1/3 from the end of the muzzle
125mm MER: 3000m
12.7mm MER: 1800m

## Slide 22: TYPE 96
125mm gun with a bore evacuator 1/3 from the end of the muzzle
ERA front glacis
Both sides of the turret has 6 smoke grenade launchers
6 road wheels with gap between #1, 2 & 3
ERA side turret
NO engine exhaus on L/S
ERA front slope
Driver sits on the L/S of hull
Gunner optics housing
Vehicle commander’s hatch w. 12.7mm MER 1800m
Meteorological data collector
Utilizes a T-72 design carousel auto-loader

## Slide 23: TYPE 99
125mm gun with a bore evacuator 1/3 from the end of the muzzle
Active high powered laser counter-measure vs. missiles
Gunner optics housing smaller
VC independent optics
Both sides of the turret has 5 smoke grenade launchers
ERA side turret
Driver sits center of the hull with 1 periscope
6 road wheels with #1 & 2 closely paired
Both sides has 1 engine exhausts
Distinct design of ERA on L/S of front glacis. Designed this way for driver exit clearance
ERA front slope
125mm MER: 3000m
AT-11b Sniper MER: 5000m
Utilizes a T-72 design carousel auto-loader

## Slide 24: TYPE 99
Gunner optics housing smaller
Utilizes a T-72 design carousel auto-loader
125mm gun with a bore
evacuator 1/3 from the end of the muzzle
VC independent optics
Both sides of the turret has 5 smoke grenade launchers
Driver sits center of the hull with 1 periscope
6 road wheels with #1 & 2 closely paired
Both sides has 1 engine exhausts
ERA front slope
7.62mm Coax MG

## Slide 25: TYPE 97
Engine exhaust
Trim vane folds down
6 road wheels that has a gap between #4, 5, and 6
Two man flat wide turret shape of a fry pan
Driver center L/S of hull
Vehicle commander
Gunner optics
Front sprocket drive supported track
30mm MER: 2000m
100mm HE & AT-10 Stabber MER: 4000m

## Slide 26: TYPE 97
Front sprocket drive supported track
Hydro propulsion system
Troop exit door
6 road wheels that has a gap between #4, 5, and
Trim vane Up
Engine exhaust

## Slide 27: ZBL 09
30mm MER: 2000m
Red Arrow-8 MER: 4000m
Side view mirrors
Each wheel has an individual wheel well
Distinct hull gap separating the #2 & 3 wheels
Speed boat type front hull
Trim vane folds on top
Headlights

## Slide 28: ZBL 09
Propellers for amphibious operations
Troop exit door
Red Arrow-8 ATGM
30mm auto-cannon
Side view mirrors
Driver L/S of hull
Engine exhaust

## Slide 29: CHALLENGER 2
Loading…
Bore evacuator 1/3 from the end of the muzzle
VC independent viewer
Gap between #5 & 6 road with 6 sets of road wheels on both sides
Rear sprocket drive supported track
Engine exhaust on both sides of hull
Sharp angle front armor turret
Stowage boxes wrap around back of turret. Vertical side armor
Gunner thermal optics on gun mantle
Driver sits center of the hull
120mm MER: 4000m
7.62mm MER: 900m

## Slide 30: CHALLENGER 2
Engine exhaust on both sides of hull
Sharp angle front armor turret
Gunner thermal optics on gun mantle
Rear sprocket drive supported track
Gap between #5 & 6 road with 6 sets of road wheels on both sides
Stowage boxes wrap around back of turret. Vertical side armor
120mm gun with bore evacuator 1/3 from the end of the muzzle

## Slide 31: WARRIOR
Sharp sloped front end
VC & Gunner optics
Driver L/S of hull 30mm MER: 1500m
7.62mm MER: 900m
Gap between #3 & 4 road wheels
Front sprocket drive supported track
Crew escape hatch

## Slide 32: WARRIOR
Front sprocket drive supported track
Engine exhaust R/S
Gap between #3 & 4 road wheels
Combat Identification Panel (CIP)
Sharp sloped front end
Rear stowage boxes are square

## Slide 33: LEOPARD 2
Leo 2A5 wedge shaped front armor
7 sets of road wheels evenly spaced
Rear sprocket drive supported track
Driver’s hatch R/S of hull
Gunner’s optics housing
Bore evacuator 2/3 from the end of the muzzle
120mm MER: 4000m
7.62mm MER: 900m

## Slide 34: LEOPARD 2
7 sets of road wheels evenly spaced
Rear sprocket drive supported track
Leo 2A4 flat vertical front armor
120mm gun with bore evacuator 2/3 from the end of the muzzle
Heater exhaust
Rear engine exhaust

## Slide 35: PUMA
Front sprocket drive supported track
Engine exhaust R/S
Gap between #3, 4 & 5 sets road wheels
VC independent optronic camera
Sharp sloped front end
Remote operated turret
Gunner optics
Driver L/S of hull
Non-amphibious IFV
30mm MER: 3000m 5.56mm MER: 800m

## Slide 36: PUMA
Front sprocket drive
supported track
Drop down troop ram
Gap between #3, 4 & 5 sets of road wheels
VC independent optronic camera
Remote operated turret with 30mm cannon
Gunner optics
Driver L/S of hull
Sharp sloped front end
Non-amphibious IFV

## Slide 37: GTK BOXER
Remote operated, can be equipped with 12.7mm or
Grenade launcher
Modular crew compartment design. It can be removed from the wheel base.
8x8 wheeled APC distinct hull gap separating the #2 &3 wheels
VC hatch
Sharp sloped front end
12.7mm MER: 1800m
40mm MER: 2212m

## Slide 38: GTK BOXER
Modular crew compartment design. It can be removed from the wheel base.
8x8 wheeled APC distinct hull gap separating the #2 &3 wheels
.50 cal MG manually operated
Sharp sloped front end
Driver hatch has ballistic windshield when driving open hatch
Engine exhaust L/S
12.7mm MER: 1800m
40mm MER: 2212m

## Slide 39: LECLERC
6 sets of road wheels evenly spaced
Rear sprocket drive supported track
VC L/S of turret with an independent thermal camera
Gunner R/S of turret with
his optics
No bore evacuator segmented
thermal shrouds
MRS collimator
Driver L/S of hull
Modular armor, designed to be unbolted and replaced if damaged in combat
Utilizes an auto-loader
120mm MER: 3000m
12.7mm MER: 1800m

## Slide 40: LECLERC
Engine exhaust L/R
Gunner R/S of turret with his optics
6 sets of road wheels evenly spaced
Rear sprocket drive supported track
120mm gun no bore evacuator segmented thermal shrouds
VC L/S of turret with an independent thermal camera
Driver L/S of hull
Modular armor, designed to be unbolted and replaced if damaged in combat
Utilizes an auto-loader

## Slide 41: VBCI
Modular armor designed to be unbolted and replaced if damaged in combat
8x8 wheeled APC with individual wheel wells for each wheel
DRAGAR one man turret that can be placed in automatic air defense mode using
25mm chain gun
VC hatch L/S of hull
Driver hatch positioned on the down slope of the hull L/S
Rear smoke grenade launchers
Non-amphibious IFV
25mm MER: 3000m
7.62mm MER: 900

## Slide 42: VBCI
DRAGAR one man turret that
can be placed in automatic air defense mode using 25mm chain gun & 7.62mm coax
Driver hatch positioned on the down slope of the hull L/S
VC hatch L/S of hull
Engine exhaust
Modular armor designed to be unbolted and replaced if damaged in combat
Bottom front end is shaped like a hammerhead shark
Rear smoke grenade launchers
Non-amphibious IFV

## Slide 43: K1A1
Turret lower silhouette in comparison to an Abrams
6 sets of road wheels on both sides
Rear sprocket drive supported track
Bore evacuator 2/3 from the end of the muzzle
Vehicle commander on the R/S with an independent viewer
Driver’s L/S of the hull
Gunner’s optics housing
Smoke grenade launchers mounted in front of turret armor
120mm MER: 4000m
.50 CAL MER: 1800m

## Slide 44: K1A1
6 sets of road wheels on both sides #3 & 5 are paired together
Rear sprocket drive supported track
120mm gun with bore evacuator 2/3 from the end of the muzzle
Vehicle commander on the R/S of the turret
Turret is tapered in the rear comparison to an Abrams
Driver’s L/S of the hull
2 rear diesel engine exhausts

## Slide 45
K21
Fully amphibious
40mm MER: 3000m
7.62mm MER: 900m
Sharp sloped front end
Driver L/S of hull
Gunner optics
6 sets of road wheels evenly spaced
Front sprocket drive supported track
2 ATGM launchers
VC independent viewer
Trim vane folds down from the bottom

## Slide 46
K21
Fully amphibious
40mm auto-cannon with cone muzzle break
Driver L/S of hull
Gunner optics
6 sets of road wheels evenly spaced
Front sprocket drive supported track
VC independent viewer
Drop down troop ram door

## Slide 47: M1A1 ABRAMS
Angular large slab armored turret
Gap between #1 & 2 road with 7 sets of road wheels on both sides
Rear sprocket drive supported track
120mm with bore evacuator 2/3 from the end of the muzzle
Vehicle commander on the R/S with
.50 CAL MG
Driver’s hatch center of hull
Gunner’s optics housing
Cylinder smoke grenade launchers indicate this is a Marine Abrams
120mm MER: 4000m
.50 CAL MER: 1800M

## Slide 48: M1A1 ABRAMS
120mm gun with bore evacuator 2/3 from the end of the muzzle
Angular large slab armored turret
Gap between #1 & 2 road with 7 sets of road wheels on both sides
Rear sprocket drive supported track
Turbine rear engine exhaust
Bustle rack and stowage boxes
Combat Identification Panels (CIP)

## Slide 49: M2/M3 BRADLEY
VC independent viewer
Gunner’s optics housing
VC hatch
7.62mm Coax MG
Tow launchers in stowed position on L/S of turret
Driver’s hatch
25mm chain gun
Final drive housings
Engine exhaust
25mm MER: 2000m
TOW MER: 3750m

## Slide 50: M2/M3 BRADLEY
Front sprocket drive supported track
Gunner’s optics housing
Tow launchers in stowed position on L/S of turret
Driver’s hatch
25mm chain gun
Gap between #3 & 4 road wheels
Combat Identification Panel (CIP)

## Slide 51: LAV-25 COYOTE
Gunner’s optics housing
Trim vane
25mm MER: 2000m
7.62mm MER: 900m
Long continuous wheel well, no hull partitions
Propellers on both rear ends of the hull
Turret is longer or turret overhang
Muffler on R/S of hull only
Driver L/S of hull
Boat shape hull

## Slide 52: LAV-25 COYOTE
Propellers on both rear ends of the hul
25mm chain gun
Boat shape hull
Turret is longer or turret overhang
Long continuous wheel well, no hull partitions

## Slide 53: STRYKER (M1126 ICV)
Storage for tire changing equipment
No propellers, non- amphibious vehicle
Inner ring in the wheel are troop step rings
Remote Weapon Station (RWS)
VC hatch
Squad leader hatch
Winch
Driver L/S of hull
Slat/Bar armor standard feature in Iraq & Afghanistan
.50cal MER: 1800m MK19 MER: 2212m

## Slide 54: STRYKER (M1126 ICV)
Engine exhaust
Slat/Bar armor standard feature in Iraq & Afghanistan
Remote Weapon Station (RWS)
Gap between #2 & 3 wheel
No propellers, non- amphibious vehicle
.50cal MER: 1800m MK19 MER: 2212m

## Slide 55: AAV
Off-center from the hull is a one man turret with a dual trunnion axis .50 cal and MK 19
Driver L/S of hull
Enhanced Armor Appliqué
.50cal MER: 1800m MK19 MER: 2212m
Trim vane

## Slide 56: Off-center from the hull is a one man turret with a dual trunnion axis .50 cal and MK 19
AAV
Enhanced Armor Appliqué Kit (EAAK
Engine exhaust
6 sets of road wheels, gap between #3 & 4
Front sprocket drive un-supported track
Both sides of the rear- end have propellers
.50cal MER: 1800m MK19 MER: 2212m

## Slide 57: M-ATV
Front engine,
rear or 4-wheel drive, 4 passenger, 4 door truck
Variants shown will have a turret or CROW
.50cal MER: 1800m MK19 MER: 2212m

## Slide 58: M-ATV
Variants shown will have a turret or CROW
Front engine,
rear or 4-wheel drive, 4 passenger, 4 door truck
.50cal MER: 1800m MK19 MER: 2212m

## Slide 59: MI-24P HIND-F
5 main rotor blades
Tail rotor is on the L/S
Bubble shaped tandem pilot canopies
Re-tractable landing gear
Twin air inlets
HIND-F has twin 30mm auto-cannons
Engine exhausts on both sides
Tail skid
Large sloped wings to mount missiles & rockets
Mid-air refueling stake
30mm MER: 4000m
AT-6 Spiral: 5000m

## Slide 60: MI-24P HIND-F
5 main rotor blades
Tail rotor is on the L/S
Bubble shaped tandem pilot canopies
Re-tractable landing gear
Large sloped wings to mount missiles & rockets
Twin air inlets
HIND-F has twin 30mm auto-cannons
Engine exhausts on both sides

## Slide 61: MI-28 HAVOC
5 main rotor blades
Under mount 30mm chain gun
Fixed wheeled landing gears
Engine exhausts on both sides of fuselage
Mouse nose radar
Armored angular shaped tandem pilot canopies
Stabilizer wing
30mm MER: 3000m
AT-6 Spiral MER: 5000m

## Slide 62: MI-28 HAVOC
Tail rotor is on the R/S
Mouse nose radar
Target sight system
High accuracy radar navigation system
Dual air inlets
Under mount 30mm chain gun
Fixed wheeled landing gears
Short sloped wing weapon load mount points
Stabilizer fin
Armored angular shaped tandem pilot canopies
30mm MER: 3000m
AT-6 Spiral MER: 5000m

## Slide 63: KA-52 HOKUM-B (Alligator)
Coaxial contra-rotating rotor blades
2 pilots sits next to each other in the canopy
Large airplane type nose to house the radar system
Re-tractable landing gears
Dual air inlets
30mm chain gun mounted on the R/S fuselage
No tail rotor
Vertical rudder
Weapon load mount wings are straight
Engine vector exhausts
30mm MER: 3000m AT-9 Vikhr MER: 10,000m

## Slide 64: KA-52 HOKUM-B (Alligator)
Coaxial contra-rotating rotor blades
2 pilots sits next to each other in the canopy
Large airplane type nose to house the radar system
Re-tractable mid-air refueling stake
Re-tractable landing gears
Air inlet
Weapon load mount wings are straight
No tail rotor Vertical rudder
Engine exhausts on both sides of fuselage
Stabilizer fins
30mm MER: 3000m AT-9 Vikhr MER: 10,000m

## Slide 65: Z-10
Stabilizer wings
Target sight system
5 main rotor blades
Chin mount 30mm chain gun
Fixed wheeled landing gears
Short aerodynamic wing weapon load mount points
Tail rotor R/S
Angular shaped tandem pilot canopies
Engine exhausts on both sides of fuselage
30mm MER: 3000m HJ-10 MER: 8000m

## Slide 66: Z-10
Stabilizer wings
Target sight system
5 main rotor blades
Chin mount 30mm chain gun
Fixed wheeled landing gears
Short aerodynamic wing weapon load mount points
Tail rotor R/S
Angular shaped tandem pilot canopies
Engine exhausts on both sides of fuselage
30mm MER: 3000m HJ-10 MER: 8000m

## Slide 67: EC-665 TIGER
Tail rotor is on the R/S
Mast mounted sight
4 main rotor blades
Dual engine exhausts
Fixed wheeled landing gears
Short sloped wing weapon load mount points
Stabilizer wings
Angular shaped step tandem pilot canopies
30mm MER: 4000m HOT MER: 4000m

## Slide 68: EC-665 TIGER
Tail rotor is on the R/S
Target sight system
4 main rotor blades
Air inlets
Dual engine exhausts
Fixed wheeled landing gears
Short sloped wing weapon load mount points
Stabilizer wings
Angular shaped step tandem pilot canopies
Chin mounted 30mm chain gun
30mm MER: 4000m HOT MER: 4000m

## Slide 69: AH-64 APACHE
Target sight system
Fixed wheeled landing gears
Tandem pilot cockpit
Air inlets
Both sides of fuselage have straight wing weapon load mount points
Engine exhausts
4 Main rotor blades
Tail rotor L/S
Synchronized elevator wing
30mm chain gun
30mm MER: 4000m
Hellfire MER: 8000m

## Slide 70: AH-64 APACHE
Target sight system
4 Main rotor blades
Fixed wheeled landing gears
Tandem pilot cockpit
Engine exhausts
30mm chain gun
30mm MER: 4000m
Hellfire MER: 8000m

## Slide 71: AH-1 COBRA
2 or 4 main rotor blades depending on variant
Tail rotor L/S
Synchronized elevator wing
Fixed landing skids
Chin mounted 20mm Gatling gun
Tandem cockpit
Slim fuselage making it faster and harder to hit
Air inlets
Engine exhausts
20mm MER: 2000m
Hellfire MER: 8000m

## Slide 72: AH-1 COBRA
Fixed landing skids
Chin mounted 20mm Gatling gun
Tandem cockpit
2 or 4 main rotor blades depending on variant
Engine exhausts
20mm MER: 2000m
Hellfire MER: 8000m