## Slide 1
PAS-13D V1 Thermal Weapon Sight
Notes: Read Slide and introduce yourself.

## Slide 2: TLO
Action: Employ a AN/PAS-13D series Thermal Sight.
Conditions: Given a fully operational AN/PAS-13D series Thermal Sight, M4A1 Carbine, M855A1 ammunition, and a 25 meter zero range.
Standards: Qualify with the AN/PAS-13D series Thermal Sight IAW TM11-5855-324-10
Notes: Read Slide

## Slide 3: Administrative
Safety: Fire Exit, Germanium Lens
Risk Assessment: Low
Environmental: Dispose of batteries in accordance with proper hazmat protocols.
Evaluation: Practical Exercises and Check on Learning
Notes: Note: Coordinate with unit hazmat certified personnel for disposal of batteries.

## Slide 4: A/N PAS-13 D
Notes: Note: Coordinate with unit hazmat certified personnel for disposal of batteries.

## Slide 6
Thermal Imaging

## Slide 7: Atmospheric Turbulence
Twinkling or shimmering (Mirage)
Affects line-of-sight through air near heated surfaces (such as air above a road heated by sunlight).
Affects stability and clarity of image (may cause image to appear to move or be unfocused).
To avoid atmospheric turbulence move to a higher position or, if possible, wait for temperatures to cool.
Notes: Instructor Note: (Atmospheric Turbulence)
Twinkling or shimmering (Mirage)
  Affects line-of-sight through air near heated surfaces (such as air above a road heated by sunlight).
  Affects stability and clarity of image (may cause image to appear to move or be unfocused).
To avoid atmospheric turbulence move to a higher position or, if possible, wait for temperatures to cool.
Scattering
  Light travels straight in a vacuum
  Light traveling through or between mediums may be bent or deflected due to:
    Reflection
    Absorption & re-emission
    Refraction (bending)

## Slide 8: Diurnal Effects
IR Radiation Intensity
Diurnal TIR radiance variations
SS= Sunset, SR = Sunrise
ENT=end of nautical twilight, BNT=beginning of nautical twilight
Scene objects heat and cool at different rates throughout the day and year.
As a result:
  TIR scene contrast varies.
  Scene objects relative temperatures may invert.
Periods will exist in these cycles where minimal TIR contrast exists (crossover points).
Note various crossover points
Notes: Instructor Note: (Diurnal & Seasonal Effects)
Diurnal Thermal Cycle
  The daily heating and cooling cycle of scene objects
  Objects absorb solar thermal energy during the day and heat up
  Objects release thermal energy at night and cool off
Seasonal Thermal Cycle
  The annual heating and cooling cycle of scene objects
  More solar energy is present in summer months hence greater thermal energy absorption and higher scene temperatures
  Less solar energy is present in winter months hence greater thermal energy release and lower scene temperatures
Instructor Note: Display and discuss slide 17 (Diurnal Effects)
Illustration of Diurnal effects
Scene objects heat and cool at different rates throughout the day and year.
As a result:
  TIR scene contrast varies.
  Scene objects relative temperatures may invert.
Periods will exist in these cycles where minimal TIR contrast exists

## Slide 9
A ROCK IN THE SUN =
A ROCK IN THE SHADE =
A ROCK ON THE SNOW =
A ROCK WITH A TEMP < ABS 0 =
THERMAL IMAGING FACTORS
EXPOSURE - AMOUNT OF IR EXPOSURE
ABSORPTION - AMOUNT OF IR ABSORBED
EMISSIVITY - RATE OF IR DISCHARGE OR HEAT
YES
YES
DEPENDENT
NO!!
ANY OBJECT WITH A TEMP ABOVE ABSOLUTE ZERO DEGREES EMITS THERMAL LIGHT (ABS 0 = -459.6º F)
Thermal Theory
Notes: Explain to the soldiers that absolute zero is equal to -459.6 degrees Fahrenheit. So, this means that everything on Earth emits thermal light.
Explain to the soldiers factors for thermal imaging:
Exposure:
a. Solar Energy:
1) Sun emits energy across entire electromagnetic spectrum
2) Energy is radiated through the earth’s atmosphere and encounters surface objects
3) Some energy is absorbed by surface objects
4) (Depending on radiant quantities of each object)
5) Some of this energy is stored as heat (thermal energy)
6) Even after the sun sets, thermal energy still remains mostly in the middle and Far IR spectrum
Absorption:
b. Heated Objects:
1) Besides radiation, thermal energy within an object can also be absorbed through conduction and convection
2) Temperature of object depends on thermal energy within object
3) Heated objects emit IR radiation
Emissivity:
c. Emissivity is how an object releases IR light
1) Different materials have different emissivity rates.
2) Objects at different temperatures can radiate the same amount (intensity) of TIR as a function of their emissivity.
3) A material with high emissivity readily absorbs thermal energy and readily emits it.
  d. IR Radiation Intensity: Intensity of IR radiation from an object depends on two factors
  1) Amount of thermal energy (heat)
  2) Emissivity of object
  Also the soldiers need to be aware that there are three ways of transferring heat. Conduction, Convection, and Radiation. Explain the differences between these in the rock example.
  Conduction: A transfer of IR energy by physical contact between two objects. (e.g. rock transferring heat into ground)
  Convection: A transfer of IR energy by a gaseous medium between two objects ( e.g. Air rising from a fire. )
  Radiation: A transfer of IR energy by being changed to electromagnetic energy and given up by radiating away from the object. (This is the mechanism which enables remote thermal sensing.)

## Slide 10: Thermal Signatures
Thermal imagers reveal temperature differences between objects and these differences lead to thermal cues
Notes: Instructor Note: (Thermal Signatures)
Thermal imagers reveal temperature differences between objects and these differences lead to thermal cues
  Engines burn fuel, produce heat and create these thermal cues in the:
    Engine compartment
    Exhaust pipes and vents
  Moving parts cause friction, produce heat and create these thermal cues in the:
    (Tracked Vehicles) tracks, road wheels, drive sprockets, support rollers, and shock absorbers
    (Wheeled Vehicles) tires, wheels, shock absorbers, drive shafts, transmissions, axles, and differentials
  Moving wheels cause disturbance of soil layers and create these thermal cues in the “freshness” of vehicle tracks
  With personnel the manner in which a target moves or dresses can reveal important information

## Slide 11
ENGINE
EXHAUST
TIRES
Thermal Cues

## Slide 12: Shadowing
A temporary thermal image left by an object. It may be:
Hot - Due to heat transference
Cool - Due to shielding an area from a heat source (in this case, the sun)

## Slide 13
What is the difference in transmission between TIR and Visible Light?
A: Visible Light is reflected from an object, TIR is Radiated from an object.
What is the Diurnal effect?
A: A time of day when the background object’s amount of radiation absorbed is equal to the amount being re-radiated.
Q. Can you see an object in TIR if it is behind a pane of glass?
A: No
Q. What is shadowing?
A. The temporary after image left by an object blocking an IR source.
Check On Learning
Notes: Note: Here are some questions to ask.

## Slide 14: Major Components
8
Notes: Read Slide

## Slide 15: Equipment Description
LTWS
Notes: READ: This slide gives you the breakdown of the major components of the PAS-13D family of sights. It also illustrates the differences between each sight. And what is common between each sight. The main difference between the LTWS and the M/HTWS is the location of the battery box. The LTWS has the battery box mounted in the side of the sight. The M/HTWS are inserted in the front through the battery compartment door.

## Slide 16: Equipment Description

## Slide 17: Equipment Description
Notes: READ: This diagram illustrates the different features between the cassettes. It also illustrates the State Of Charge(SOC) indicator. Which allows the operator to determine the amount of charge left in his batteries without turning on the sight. This feature will only work with the L91 AA Lithium batteries.

## Slide 18: Equipment Description
State of Charge INDICATOR ONLY WORKS WITH L91 AA LITHIUM BATTERIES
Notes: READ: This diagram illustrates the different features between the cassettes. It also illustrates the State Of Charge(SOC) indicator. Which allows the operator to determine the amount of charge left in his batteries without turning on the sight. This feature will only work with the L91 AA Lithium batteries.

## Slide 19
NOTE: IF BATTERY LOW LIGHT COMES ON AFTER INSTALLATION CHECK FOR CORROSION.
GASKET
CONTACTS
BATTERY
CASSETTE
PMCS

## Slide 20: Equipment Description
Notes: READ: This gives you an idea of the difference in size between the lenses of the PAS-13D.

## Slide 21
CONTROLS
Hold FOV / MODE to access the menu system
Use the GAIN / BRT buttons to scroll through sub-menus
Use the FOV/MODE button to select MENU items
Selecting the Up Arrow will return the user to the display main menu
Selecting the X function allows the user to exit all on-screen menus
Notes: READ: This shows the location of all the indicators shown on the display screen in the PAS-13D.
Reticle Properties:
  Is digitally generated, selectable and adjustable.
  Is the only thing moved during alignment (no mechanical movement).
  Coordinates are stored separately for each reticle pattern.
  Coordinates are retained through ON/OFF cycling and battery changes - no power source is required to retain reticle position.
TWS zero/sight alignment is retained through mount/dismount cycles if al the following conditions occur:
  Same weapon
  Same TWS
  Same rail slot
  Same reticle coordinates

## Slide 22
WHEN MENU IS OFF, THIS WILL
ADJUST YOUR LEVEL OF GAIN. GAIN
AFFECTS THE TWS SENSETIVITY TO
DIFFERENT TEMPERATURES.
WHEN MENU IS OFF, THIS WILL
ADJUST YOUR DISPLAY SCREENS BRIGHTNESS.
BRIGHTNESS DOES NOT AFFECT THE THERMAL
SCENE, ONLY THE BRIGHTNESS OF THE DISPLAY SCREEN.
PRESS TO ADJUST POLARITY FROM WHITE HOT TO BLACK HOT
CONTROLS
Notes: READ: In order to select a reticle, you must depress and hold the FOV/MODE switch for >1 second then release to pull up the main menu.
To navigate the menus, you tap the BRT or GAIN switches to move through the selections.
Tapping for < 1 second will select menu options.
In order to adjust the contrast or brightness manually, use the BRT or GAIN switches to make necessary adjustments. When adjusting the brightness or gain manually, turn them both down all the way, and bring them up slowly until you have a clear picture.

## Slide 23
TO INITALLY CALIBRATE IMAGE, HOLD BOTH GAIN AND BRT SWITCHES FOR >1 SECOND ON UNIFORM BACKGROUND.
TO CHAGE BETWEEN WIDE FIELD OF VIEW (WFOV) AND NARROW FIELD OF VIEW (NFOV). TAP ON THE FOV BUTTON
CONTROLS
Notes: READ: In order to select a reticle, you must depress and hold the FOV/MODE switch for >1 second then release to pull up the main menu.
To navigate the menus, you tap the BRT or GAIN switches to move through the selections.
Tapping for < 1 second will select menu options.
In order to adjust the contrast or brightness manually, use the BRT or GAIN switches to make necessary adjustments. When adjusting the brightness or gain manually, turn them both down all the way, and bring them up slowly until you have a clear picture.

## Slide 24
Reticle Selection
Notes: READ: This gives you an example of how the reticle can be used for estimation of size and angle. The distance between the two horizontal stadia lines represents the width of an average man (19 Inches) at 25 m. The distance between the vertical stadia lines represents the height of a 5’ (60 inches) man at 300 m. The dot at the middle is the point of aim for the M4/16 series through 300 meters.

## Slide 25
WFOV
1.36 X MAGNIFICATION
NFOV
2.71 X MAGNIFICATION
M4/M16 RETICLE
WINDAGE AND ELEVATION ADJUSTMENTS ARE HALVED WHILE IN NFOV FOR THE LTWS. AND 1/3 FOR THE M/HTWS.
NOTE THAT THE STADIA LINES INDICATE WHAT YOU WILL BE SEEING IN THE NARROW FIELD OF VIEW.

## Slide 26
RETICLE ADJUST
PRESS AND HOLD IN DIRECTION OF IMPACT WHEN IN ZERO/RETICLE MODE.
UP
DOWN
LEFT
RIGHT
0 0
L5
R5
U 5
D 5
THE OPERATOR MUST ADJUST WHILE IN ZERO MODE.
Notes: READ: When adjusting the reticle, it is important to note that any adjustment made to the sight in these directions adjusts the point of impact. There is no physical adjustment to the optic at all. All the ‘clicks’ are digitally adjusted by the sight to move the point of impact. And the operator must select the OPERATE mode to take sight out of ZERO mode unlike the PAS-13B.

## Slide 27
Extended Battery Life
Notes: READ: This shows you how the PAS-13D is different from the previous models. This is the E

## Slide 28
Check On Learning
What does each circle on the state of charge indicator represent?
1/6th of the battery life.
What is the preferred battery for the PAS-13D?
L91 AA Lithium, 4 each for LTWS, 6 each for M/HTWS.
Notes: NOTE: Ask for questions and then conduct a check on learning by asking question and then summarize the learning activity.
Question: What is the preferred battery for the PAS-13D?
Answer: L91 AA Lithium, 4 each for LTWS, 6 each for M/HTWS.
Question: What do you use the Objective Focus Ring for?
Answer: Adjusting the Image
Question: What purpose is the Eyecup assy. Used for?
Answer: To turn on and off the Display screen

## Slide 29
NOTE: TIGHTEN RAIL GRABBER TWO CLICKS.
M4/ M16A4
Mounting TWS

## Slide 30
M4 MWS
Place fingers over ovals on both sides of black dot to create a heat source.
Place zeroing aim point in center of black dot (in between the two fingers).
Move borelight laser to it’s gray dot by making adjustments to the TWS.
Continue to make adjustments until the borelight laser is centered in it’s gray dot.
NOTE: BORESIGHTING ONE FOV BORESIGHTS BOTH FOVS.
Stabilizing the weapon is crucial.
Zero borelight.
10M Bore Sighting
Notes: READ: The PAS-13D is borelighted by putting the reticle on the defined point of aim, calculating the corrections necessary to adjust the borelight (Point of Impact) into it’s designated Spot. Making the corrections, then bringing the reticle back on point of aim and repeating. The reason for this is thermal sights do not make visible adjustments on the screen. So it is not possible to put the borelight on it’s target and then adjust the thermal to it’s position.

## Slide 31
NOTE: RETIGHTEN AFTER INITIAL 5 ROUND SHOT GROUP.
M16A4, M4 AND MWS M16A2
POINT OF AIM
POINT OF IMPACT
M16A2 25m TARGET
3.8 SQUARES (3.4cm)
8.1 SQUARES (6.5 cm)
Zeroing Procedures
Notes: READ: Note that one major difference between the PAS-13B and PAS-13D is that an adjustment made in one FOV adjusts the other FOV. And the preferred method of zeroing is to adjust the sight in NFOV and then confirm in WFOV. The reason for this is in WFOV, the LTWS moves 2 ‘clicks’ for every ‘click’ adjusted. And in the M/HTWS, the reticle moves 3 ‘clicks’ for every ‘click’ adjusted in WFOV.

## Slide 32
Zeroing Procedures
MTWS
WFOV 1click = 2 MOA
NFOV 2 clicks = 1/2 MOA
M16/M4 SERIES
LTWS
WFOV 1click=2.5 cm @ 25M
NFOV 2 click=1.25cm@ 25m

## Slide 33
DISPLAY WILL NOT COME ON
DISPLAY IS BLURRY
FOV IS TOO DARK CAN NOT SEE OBJECTS
CAN NOT TELL ONE OBJECT FROM ANOTHER
DISPLAY IS NOT FOCUSED, TARGET IS BLURRY
RETICLE WILL NOT CHANGE
WINDAGE/ELEVATION WILL NOT CHANGE
BATTERY KEEPS GOING DEAD
BATTERY LOW LIGHT COMES ON IMMEDIATELY
Battery Is Dead
ADJUST DIOPTER FOCUS RING.
ADJUST BRIGHTNESS.
ADJUST GAIN.
ADJUST THE OBJECTIVE FOCUS RING.
CHOOSE RETICLE SELECT MENU.
ENSURE SIGHT IS IN RETICLE ADJUST MODE.
ENSURE EMERGENCY MODE IS OFF.
CHECK FOR CORROSION.
PMCS: Trouble Shooting