## Slide 2: TERMINAL LEARNNG OBJECTIVE
Action: Conduct introduction to Image Intensifier (I2) and Laser devices with the AN/PVS 14 (MNVD) and AN/PEQ-15 (APTIAL).
Conditions: Record fire range at night, selected weapon, NVGs and laser aiming device.
Standards: Obtain at least 14 target hits out of 20 timed targets

## Slide 3
Safety Requirements:
Risk Assessment:
Environmental Considerations:
Evaluation:

## Slide 4: ENABLING LEARING OBJECTIVE A
Action: Identify characteristics of the AN/PVS 14.
Conditions: Given a AN/PVS 14 and 2 fresh AA batteries.
Standards: Identify components of the AN/PVS14 accordance with.
Notes: Explain: the major components of the NVGs, their functions and importance. Briefly explain how the 7B/D can use AA or BA5567( hocky puck style battery, tit up when inserting.

## Slide 5
Principles of Operation:
The goggles collect the available light from a scene illuminated by the night sky and project an intensified image into the operator's eye in the proper perspective. An internal electronic circuit controls the battery power to the image intensifier and IR illumination source. The circuit also monitors the battery voltage and activates an indicator light when the voltage is low. The goggles accommodate various operational requirements and differences in physical characteristics of the individual operators.

## Slide 6: Extreme Darkness
Night vision requires some ambient light to work
In total darkness, artificial illumination must be used
Notes: Image intensification night vision will not work in the total absence of light, at the bottom of a cave, for instance. As we now know, this light does not have to be light in the visible wavelength, but there must be some source of light or photons for the night vision to function correctly.
When you must operate in extremely dark conditions, a supplemental light source may be required. Under most conditions, a near IR light source is preferable to a visible light source since visible light could give away the goggle wearer’s location and provide light for the bad guys. There are many supplemental IR light sources available to the law enforcement user. Most military goggles like the PVS-7 and PVS-14/6015 are equipped with built-in IR illuminators for close range requirements. There are also a variety of IR beacons and signaling devices that can be quite useful in a variety of tactical situations.
Scintillation is a faint, random, sparkling effect throughout the image area. Scintillation, sometimes called “video noise,” is a normal characteristic of microchannel plate image intensifiers and is more pronounced under low-light conditions. Seeing it is an indicator that you need to consider using supplemental illumination, as described above.

## Slide 7
Weight: 15 ounces
Battery: Operating within -4/70F PVS 14 2(AA) lithium batteries with zero IR usage 60/70 hrs. With 10% IR usage 55/65 hrs of use 7B/D BA-5567 or 2(AA)
Range: starlight/Moonlight: 150m/300m
Magnification 1x or x3 with magnifier
Actual range depends on light conditions
Characteristics

## Slide 8
On-Off-IR Pull Switch: this controls the goggles and IR illuminator power.
Monocular Tube: This image intensification tube amplifies available light.
Objective Lens: This lens focuses the light of the image intensifier.
Objective Lens Cap: this cap protects the Objective Lens
Objective Focus: Used to focus your eyes within the compensation range of 25cm to infinity
Diopter Adjustment Ring: focuses eyepiece lens for each eye without the need for glasses. Adjusts for sharpest image of intensifier screen
IR Illuminator: This provides light for viewing up to 3 meters in low ambient light conditions for reading instruments or maps at night.
Major Components

## Slide 9
9) Battery Compartment: Houses the various batteries( Only AA or BA-5567)
10) Eye Piece Lens Cap: Protects the eyepiece lens and prevents light from leaking around the eyepiece.
11) Demisting Shields: These are used to prevent the eyepiece lenses from becoming fogged.
12) High-Light Detector: Automatically shuts off the goggles after 70 seconds +/- 30 seconds in daylight or bright room light.
13) Latch: Used to separate the goggle assembly from the head or Kevlar assembly. IF on the goggles will automatically shut off when separated from the mount.
14) Head Mounting Assembly: Mounts the NVG’s to the soldiers head to allow hands free operation.
15) Helmet Mounting Assembly: Mounts NVG’s to soldiers kevlar to allow hands free operation.
Major Components

## Slide 10
Objective Lens
Intensifier Tube
Eyepiece
ON/OFF Switch
Variable Gain
Basic Night Vision System
Notes: A basic system consists of:
1. An objective lens that collects light you cannot see with your unaided eye, and focuses it on an image intensifier tube
2. An image intensifier tube to amplify the image
An eyepiece to present a visible view to the eye
An ON/OFF/IR Switch
An variable gain control.
Canada is the first Army to purchase the single-battery PVS-14. The changes to the PVS-14 are relative minor in that only the lower housing is affected. The evolution to a single battery system has improved the robustness and reliability of the system by redesigning the battery cap and battery compartment.
(NOTE: This is a good time to have the student take out their unit and show them how to operate it)

## Slide 11
OFF- The storage/non use position resets goggles after automatic shutoff
ON- The goggles will operate continuously
IR-PULL- Turns on the IR beam, will stay on till turned off. Pull out and turn

## Slide 12
Standard Kit with Optional Accessories
Notes: These are the parts included, those circled in red are optional items. The standard parts include- night vision device with eyecup, neck cord and objective lens cap – carry pouch – head mount – head mount adapter – helmet mount – demist shield – sacrificial window – operator’s manual – user’s card - lens paper – AA alkaline batteries.
Optional items include - 3X magnifier with adapter, compass, small arms adapter and binocular mount.
Instructor Note: Now would be a good time for the students to take the items out of the field pouch and famaliarize themselves with these items.

## Slide 13
Action: Perform PMCS on PVS14’s
Condition: Given an NVG, lens cloth and fresh batteries
Standards: Perform maintenance on an NVG IAW
Terminal Learning Objective B

## Slide 14
Action: Mount PVS-14’s into operating configuration
Conditions: Given a PVS-14, Head mount assembly, or Kevlar assembly and 2 fresh AA batteries.
Standards: properly mount the PVS-14’s onto given mount assembly within 5 minutes.
Terminal Learning Objective C

## Slide 15: Helmet Mount
Helmet Mount

## Slide 16
THE SHARPEST IMAGE WILL BE OBSERVED ONLY WHEN THE OBJECTIVE LENS AND EYEPIECE ARE PROPERLY FOCUSED
THESE ADJUSTMENTS OPERATE INDEPENDENTLY AND MUST BE MADE SEPERATELY

## Slide 17
Interpupillary Adjustment
(AN/PVS7’s only)
Diopter Adjustment
Objective Focus
** Any adjustment to the head strap requires eye relief adjustment
Order of Adjustments

## Slide 18
Used to focus the eyes (with or without glasses) to the image intensification screen
Diopter Adjustment
Diopter Adjustment AN/PVS-14

## Slide 19
Adjust for sharpest view of image being viewed
Lens Focus
Objective Lens Focus Knob AN/PVS-14

## Slide 20
Variable Gain
Adjusts the illumination input to the eye
Variable Gain Control AN/PVS-14

## Slide 21
FOR OPTIMUM PERFORMANCE
Adjust the television before turning the channels!!!

## Slide 22: Questions ?

## Slide 23: PEQ-15 This system allows you faster target acquisition times in day and nighttime operations in order to kill the enemy.

## Slide 24
Action: Identify how to operate the PEQ-15,
Identify system functions and safety precautions.
Conditions: Given in a classroom environment
with all required materials and equipment.
Standard: The student will have knowledge to operate the PEQ-15 correctly; understand the various system functions ,and safety precautions.

## Slide 25: PEQ-15 This system allows you faster target acquisition times in day and nighttime operations in order to kill the enemy.

## Slide 26
The PEQ-15 is a rugged multifunction laser device that emits both visible and infrared(IR) light for precise weapon aiming and target/area illumination.

## Slide 27
Danger
Invisible Laser Radiation-Avoid Direct Exposure to the Beam
Do not stare into the infrared laser beam.
Do not look into the infrared laser beam through Binoculars or telescopes.
Do not point the infrared laser beam at mirror like surfaces.
Do not shine the infrared laser beam into peoples eyes.

## Slide 28
Do not store with batteries installed.
High Power modes are not eye safe and are blocked with a (Blue)safety screw.
All high power modes shall not be used for force-on-force training.

## Slide 29
The PEQ-15 provides the following capabilities:
Stand-Alone and Dual Modes to include:
Visible Aiming Laser
Infrared Aiming Laser
Infrared Illuminator
Momentary or Constant ON Activation
Remote Switch Activation
Programmable Illuminator Pulse Rate
Mounts to MIL-STD-1913 mounting rail of the host weapon.

## Slide 30
The PEQ-15 is designed for operation in battlefield environments for precise weapon aiming, target marking and illumination.

## Slide 31
Item Description
1. Soft Carrying Case
2. Operator and Unit Maintenance man.
3. Quick Reference Guide
4. PEQ-15 Assembly
5. Pattern Generators (setof5)
6. Remote Cable Switch
7. Tape Fastener (3)
8. Strap, Retaining(2)
9. Battery ,3-Volt Lithium

## Slide 32
Weight: 7.5 ounces (with one DL123A Battery installed)
Length:
4.6inches
Width:
2.8inches
Height:
1.6inches

## Slide 33
Visible Aim Laser
Range: >25m
IR Aim Laser
Range: >600m (Low)
Range: >2000m (High)
IR Illuminator
Range: >600M (Low)
Range: >2000M (High)

## Slide 34
Power and Performance
Batteries
One 3-volt DL123A Lithium
Battery Life
>6 hours in Dual Hi
Waterproof
6 meters for 1hour

## Slide 35
1. Aim Laser Exit Port Cover
2. Mode selector switch
3. Illuminator adjusters
4. Illuminator Diffuser
5. Illuminator focus knob
6. IR Aim Laser
7. Visible Aim Laser

## Slide 36
14.Integral Rail Grabber Bracket
13. Tie down point
15. Safety Screw
16. Remote Jack
17. Lanyard Attachment Point
8. Battery Cap/Compartment
9. Safety Screw Storage
10. LED Status Indicator
11. Activation Button
12. Aim Laser Adjustment

## Slide 37
1. Vis Aim Low (VIS-AL)–The visible aiming beam operates at LOW power.
2.Off (O) –The ATPIAL will not operate
3.Program(P) –Program Mode
4.IRAimLow (IR-AL) –The infrared aiming beam operates at LOW power.
5.IRDualLow (IR-DL) –The infrared aiming beam and infrared illuminator operates at LOW Power.
6.IRAimHigh (IR-AH)–The infrared aiming beam operates at HIGH power.
7.IRIllumHigh(IR-IH)–The infrared illuminator operates at HIGH power.
8.IRDualHigh(IR-DH)–The infrared aiming beam and infrared illuminator operates at HIGH power

## Slide 38
MOUNTING TO M-4
Loosen the clamping knob on the PEQ-15 Rail Grabber until it has sufficient space to fit over the rail.
Secure the recoil lug of the ATPIAL Rail Grabber to the rail by applying down ward and forward pressure to take out the slack then turning the slotted knob CW finger tight.
Tighten the clamping knob with a coin or multipurpose tool ½ of a complete turn or 180 degrees to ensure proper seating.

## Slide 39
Adjustments ½
MOA per click
Elevation knob
Windage knob
CW is: up
CCW: down
CW: right
CCW: left
Illuminator knob
Elevation CW: up
CCW: down
Windage CW: right
CCW: left

## Slide 40
Zero Offset for top mounted PEQ-15

## Slide 41
QUESTIONS?